HAMPSHIRE COUNTY, WEST VIRGINIA

Planning Office

90 N. High Street

PO Box 883

Romney, WV

304-822-7018

MIDDLE DEPARTMENT INSPECTION AGENCY, INC.

# MINIMUM OF 24 HOUR NOTICE REQUIRED

Single Family Inspection Procedures

- Building permit must be posted on the work site and clearly visible from the road until completion of the project.

- Your approved plans must be available at all times for inspections.  These plans were submitted with your application and were marked “Subject to Field Approval” by the building inspector.

- The permit applicant or authorized agent is responsible for scheduling all inspections.

- DO NOT schedule an inspection if the work is not ready!

Inspection Schedule

- Footing inspection – To be done after forming and prior to placing of concrete.

800-248-MDIA (6342)

- Foundation inspection – French drain and water-proofing prior to backfilling and seal plate, before any framing.

800-248-MDIA (6342)

- Plumbing under slab (rough-in) done prior to placing concrete floor which can be done at foundation inspection.

800-248-MDIA (6342)

- Framing inspection – Done prior to insulating, but after heating, plumbing and wiring are roughed in and pressure test are in place for all plumbing systems, and prior to any exterior finishes being applied.

800-248-MDIA (6342)

- Wallboard if fire rated construction is required.

800-248-MDIA (6342)

- Final inspection of building, plumbing and electrical  – When job is completely finished, prior to occupancy permit

800-248-MDIA (6342)